## Slide 1: DIGITAL ELECTRONICS III Semester CSE, CSE (AIML) & CSE (DS)
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
SCHOOL OF ENGINEERING & TECHNOLOGY
GIET UNIVERSITY, GUNUPUR, ODISHA
Dr. Ajit Kumar Patro

## Slide 2: LOGIC LEVELS AND PULSE WAVEFORMS LOGIC GATES

## Slide 3: Logic Levels and Pulse Waveforms
Digital systems use the binary number system. Therefore, two-state devices are used to represent the two binary bits 1 and 0 by two different voltage levels, called HIGH and LOW.
If the HIGH voltage level is used to represent 1 and the LOW voltage level to represent 0, the system is called the positive logic system.
If the HIGH voltage level is used to represent 0 and the LOW voltage level to represent 1, the system is called the negative logic system.

## Slide 4
Normally, the binary 0 and 1 are represented by the logic voltage levels 0 V and + 5 V.
In a positive logic system, 1 is represented by + 5 V (HIGH) and 0 is represented by 0 V (LOW).
In a negative logic system, 0 is represented by + 5 V (HIGH) and 1 is represented by 0 V (LOW).

## Slide 5
In reality, because of circuit variations, the 0 and 1 would be represented by voltage ranges instead of particular voltage levels.
Usually, any voltage between 0 V and 0.8 V represents the logic 0 and any voltage between 2 V and 5 V represents the logic 1.
The range between 0.8 V and 2 V is called the indeterminate range. If the signal falls between 0.8 V and 2 V, the response is not predictable.

## Slide 6
A pulse may be a positive pulse or a negative pulse.
A single positive pulse is generated when a normally LOW voltage goes to its HIGH level and then returns to its normal LOW level.
A single negative pulse is generated when a normally HIGH voltage goes to its LOW level and then returns to its normal HIGH level.

## Slide 9
The rise time is defined as the time taken by the pulse to rise from 10% to 90% of the pulse amplitude.
The fall time is defined as the time taken by the pulse to fall from 90% to 10% of the pulse amplitude.
The duration of the pulse is usually indicated by pulse width tw which is defined as the time between the 50% points on the rising and falling edges.

## Slide 10
In digital systems the waveforms are composed of a series of pulses and can be classified as periodic waveforms and non-periodic waveforms.
A periodic waveform is one which repeats itself at regular intervals of time called the period, T.
A non-periodic waveform, of course, does not repeat itself at regular intervals and may be composed of pulses of different widths and/or differing time intervals between the pulses.

## Slide 11
The reciprocal of the time period is called the frequency of the periodic waveform.
Duty cycle of a periodic pulse waveform is the ratio of the ON time (pulse width tw) to the period of the pulse waveform.

## Slide 12: Example: A periodic digital waveform has a pulse width of 25 μs and a period of 150 μs. Determine the frequency and the duty cycle.
Solution:
Pulse width tw = 25 μs and period T = 150 μs
Frequency

## Slide 13: Example: A portion of a periodic digital waveform is shown in Figure. The measurements are in milliseconds. Determine (a) period (b) frequency and (c) duty cycle.
Solution:
Period T = 10 ms

## Slide 14: Logic Gates
Logic gates are the basic building blocks of any digital system.
It is an electronic circuit having one or more than one input and only one output.
The relationship between the input and the output is based on a certain logic.
Based on this, logic gates are named as NOT, AND, OR, NAND, NOR, EX-OR and EX-NOR gate.

## Slide 15: Types of Logic Gates

## Slide 16: Buffer
A buffer, is a basic logic gate that passes its input, unchanged, to its output.
The main purpose of a buffer is to regenerate the input, usually using a strong high and a strong low.
A buffer has one input and one output; its output always equals its input.
Its symbol is simply a triangle.
Boolean Expression:

## Slide 17
7407 Hex Buffer
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 18: NOT Gate
The NOT gate is an electronic circuit that produces an inverted version of the input at its output.
It is also known as an inverter.
If the input variable is A, the inverted output is known as NOT A.
This is also shown as A' or
Boolean Expression:

## Slide 19
7404 Hex Inverter
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 20: AND Gate
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high.
A dot (.) is used to show the AND operation.
Boolean Expression:

## Slide 21
7408 Quad 2-input AND Gate
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 22: OR Gate
The OR gate is an electronic circuit that gives a high output (1) if one or more of its inputs are high.
A plus (+) is used to show the OR operation.
Boolean Expression:

## Slide 23
7432 Quad 2-input OR Gate
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 24: NAND Gate
This is a NOT-AND gate which is equal to an AND gate followed by a NOT gate.
The outputs of all NAND gates are high if any of the inputs are low.
The symbol is an AND gate with a small circle on the output. The small circle represents inversion.
Boolean Expression:

## Slide 25
7400 Quad 2-input NAND Gate
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 26: NOR Gate
This is a NOT-OR gate which is equal to an OR gate followed by a NOT gate.
The outputs of all NOR gates are low if any of the inputs are high.
The symbol is an OR gate with a small circle on the output. The small circle represents inversion.
Boolean Expression:

## Slide 27
7402 Quad 2-input NOR Gate
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 28: EX-OR Gate
The 'Exclusive-OR' gate is a circuit which will give a high output if either, but not both, of its two inputs are high.
An encircled plus sign ( ) is used to show the EX-OR operation.
Boolean Expression:

## Slide 29
7486 Quad 2-input EX-OR Gate
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 30: EX-NOR Gate
The 'Exclusive-NOR' gate circuit does the opposite to the EX-OR gate.
It will give a low output if either, but not both, of its two inputs are high.
The symbol is an EX-OR gate with a small circle on the output. The small circle represents inversion.
Boolean Expression:

## Slide 31
74266 Quad 2-input Ex-NOR Gate
Graphic Symbol
IEEE Symbol
Truth Table

## Slide 32: Digital Logic Gate Truth Table Summary

## Slide 33
EX-OR Gate
EX-NOR Gate

## Slide 34: 3-input Ex-OR Gate
The logic function implemented by a 2-input Ex-OR is given as either: “A OR B but NOT both” will give an output at Q. In general, an Ex-OR gate will give an output value of logic “1” ONLY when there are an ODD number of 1’s on the inputs to the gate. Then an Ex-OR function with more than two inputs is called an “odd function”.