## Slide 1: DIGITAL ELECTRONICS III Semester CSE, CSE (AIML) & CSE (DS)
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING
SCHOOL OF ENGINEERING & TECHNOLOGY
GIET UNIVERSITY, GUNUPUR, ODISHA
Dr. Ajit Kumar Patro

## Slide 2: AXIOMS AND LAWS OF BOOLEAN ALGEBRA

## Slide 3: Boolean Algebra
Boolean Algebra is used to analyze and simplify the digital (logic) circuits.
It uses only the binary numbers i.e. 0 and 1.
It is also called as Binary Algebra or logical Algebra.
Algebra consists of symbolic representation of a statement (generally mathematical statements).
Similarly, there are expressions, equations and functions in Boolean algebra as well.

## Slide 4: Axioms or Postulates of Boolean Algebra
Axioms or postulates of Boolean algebra are a set of logical expressions that we accept without proof and upon which we can build a set of useful theorems.
Actually axioms are nothing more than the definitions of three basic logic operations that we have already discussed: AND, OR, INVERT.

## Slide 5
OR Operation
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT Operation
AND Operation
0 . 0 = 0
0 . 1 = 0
1 . 0 = 0
1 . 1 = 1

## Slide 6
1. Postulate 2 : Identity
(a) (b)
2. Postulate 5 : Complement
(a) (b)
3. Theorem 1 : Idempotent
(a) (b)
4. Theorem 2 : Annulment
(a) (b)
5. Theorem 3 : Involution

## Slide 7
Theorem 1
(a) A + A = A
A + A = (A + A).1
= (A + A).(A + A’)
= A + A.A’
= A + 0
= A
(b) A.A = A
A.A = A.A + 0
= A.A + A.A’
= A.(A + A’)
= A.1
= A

## Slide 8
6. Postulate 3 : Commutative Law
(a) A + B = B + A

## Slide 9
(b) A.B = B.A

## Slide 10
7. Theorem 4 : Associative Law
(a) (A + B) + C = A + (B + C)

## Slide 11
(b) (A.B).C = A.(B.C)

## Slide 12
8. Postulate 4 : Distributive Law
(a) A.(B + C) = A.B + A.C

## Slide 13
(b) A + B.C = (A + B).(A + C)
RHS = (A + B).(A + C)
= A.A + A.C + B.A + B.C
= A + A.C + A.B + B.C
= A.(1 + C + B) + B.C
= A.1 + B.C
= A + B.C = LHS

## Slide 15
9. Theorem 6 : Absorption
(a) A + A.B = A
A + A.B = A.1 + A.B
= A.(1 + B) = A.1 = A

## Slide 16
(b) A.(A + B) = A
A.(A + B) = A.A + A.B = A + A.B
= A.(1 + B) = A.1 = A

## Slide 17
10. Consensus Theorem
Proof:

## Slide 18
11. Transposition Theorem
Proof:

## Slide 19: 12. De Morgan’s Theorem
De Morgan’s Theorem states that
The complement of a sum of variables is equal to the product of their individual complements.
The complement of the product of variables is equal to the sum of their individual complements.

## Slide 22: Duality
It states that every algebraic expression deducible from the postulates of Boolean algebra remains valid if the operators and identity elements are interchanged.
If the dual of a algebraic expression is desired, we simply interchanged OR and AND operators and replace 1’s by 0’s and 0’s by 1’s.

## Slide 23
Prove that the dual of EX-OR gate is equal to its complement.
EX-OR gate : A . B’ + A’ . B
Dual of EX-OR gate : (A + B’) . (A’ + B)
= A.A’ + AB + B’A’ + B’B
= 0 + AB + B’A’ + 0
= AB + A’B’
Complement of EX-OR gate
(AB’ + A’B)’ = (AB’)’ . (A’B)’ = (A’ + B).(A + B’)
= A’A + A’B’ + BA + BB’
= 0 + A’B’ + BA + 0 = AB + A’B’